| 1. | The_____layer of the TCP/IP protocol suite provides service for end users. |
| --- | --- |
|  | (A) | data-link | (B) | transport | (C) | application |
|  | (D) | physical |  |  |  |  |
| 2. | The_____layer of the TCP/IP protocol suite transmits a bit stream over a physical medium. |
|  | (A) | physical | (B) | data-link | (C) | network |
|  | (D) | transport |  |  |  |  |
| 3. | The_____layer of the TCP/IP protocol suite is responsible for node-to-node delivery of a frame between two adjacent nodes. |
|  | (A) | transport | (B) | network | (C) | data-link |
|  | (D) | session |  |  |  |  |
| 4. | According to the von Neumann model, ______ |
|  | (A) | only data is | (B) | only programs are |  |  |
|  | (C) | data and programs are | (D) | none of the above |  |  |
| 5. | Which of the following is equivalent to 24 in decimal? |
|  | (A) | [11000]2 | (B) | [1A]16 |  |  |
|  | (C) | [31]8 | (D) | none of the above |  |  |
| 6. | The _____ protocol is one of the protocols in the transport layer. |
|  | (A) | TCP | (B) | UDP | (C) | SCTP |
|  | (D) | all of the above |  |  |  |  |
| 7. | _____ is a protocol for file transfer. |
|  | (A) | FTP | (B) | SMTP | (C) | TELNET |
|  | (D) | HTTP |  |  |  |  |
| 8. | _____ is a protocol for accessing and transferring documents on the WWW |
|  | (A) | FTP | (B) | SMTP | (C) | TELNET |
|  | (D) | HTTP |  |  |  |  |
| 9. | Which of the following IP addresses fall into the CIDR block of 115.64.4.0/22? |
|  | (A) | 115.64.8.32 | (B) | 115.64.7.64 | (C) | 115.64.3.255 |
|  | (D) | 115.64.12.128 |  |  |  |  |
| 10. | Which of the following IP addresses can be assigned to the host devices? |
|  | (A) | 205.7.8.32/27 | (B) | 191.168.10.2/23 | (C) | 127.0.0.1/8 |
|  | (D) | 203.123.45.47/28 |  |  |  |  |

| 11. | Without converting, find the minimum number of digits needed in the destination system for Four-digit decimal converted to octal. |
| --- | --- |
|  | (A) | 5 | (B) | 6 | (C) | 7 |
|  | (D) | 8 |  |  |  |  |
|  | 〈背面尚有試題，請翻頁〉 |
| 12. | Change 534 to 16-bit two’s complement integers. |
|  | (A) | 0000001000110110 | (B) | 0000001000010111 |  |  |
|  | (C) | 0000001000010110 | (D) | 0000001001010110 |  |  |
| 13. | The 01110111 is sign-and-magnitude binary number in an 8-bit allocation. Convert this number to decimal. |
|  | (A) | +119 | (B) | -119 | (C) | +120 |
|  | (D) | -120 |  |  |  |  |
| 14. | For the binary ______ operator, if the input is two 1s, the output is 0. |
|  | (A) | AND | (B) | OR | (C) | XOR |
|  | (D) | All of the above |  |  |  |  |
| 15. | The data in ______ is erased if the computer is powered down. |
|  | (A) | RAM | (B) | ROM | (C) | A tape drive |
|  | (D) | A CD ROM |  |  |  |  |
| 16. | ______ is a step-by-step method for solving a problem or doing a task. |
|  | (A) | A construct | (B) | A recursion | (C) | An iteration |
|  | (D) | An algorithm |  |  |  |  |
| 17. | ______ is a basic algorithm that arranges data according to its value. |
|  | (A) | Inquiry | (B) | Sorting | (C) | Searching |
|  | (D) | Recursion |  |  |  |  |
| 18. | ______ is an English-language-like representation of code. |
|  | (A) | A UML diagram | (B) | A program | (C) | Pseudocode |
|  | (D) | An algorithm |  |  |  |  |
| 19. | Find how many times the statement in the following code segment in C is executed. A=5 do { statement; A=A+1; } while (A<10); |
|  | (A) | 4 | (B) | 5 | (C) | 6 |
|  | (D) | ∞ |  |  |  |  |
| 20. | Find how many times the statement in the following code segment in C is executed. A=5 While (A < 8) { statement; A=A-2; } |
|  | (A) | 4 | (B) | 5 | (C) | 6 |
|  | (D) | ∞ |  |  |  |  |
|  | 〈背面尚有試題，請翻頁〉 |
| 21. | Find how many times the statement in the following code segment in C is executed. For (int i=5; i<20, i++) { statement; I=i+1; } |
|  | (A) | 8 | (B) | 9 | (C) | 10 |
|  | (D) | ∞ |  |  |  |  |
| 22. | The ________ is a computer subsystem that performs operations on data. |
|  | (A) | CPU | (B) | Memory | (C) | I/O Hardware |
|  | (D) | None of the above |  |  |  |  |

| 23. | Change the 4 13/64 into binary. |
| --- | --- |
|  | (A) | (0100.0011010)2 | (B) | (0101.0011010)2 | (C) | (0100.0011011)2 |
|  | (D) | (1100.0011010)2 |  |  |  |  |
| 24. | Show the result of [(99)16 AND (33)16] OR [(00)16 AND (FF)16] |
|  | (A) | (9)16 | (B) | (10)16 | (C) | (11)16 |
|  | (D) | (12)16 |  |  |  |  |
| 25. | Convert +23x1.111111 in 32 bit IEEE format. |
|  | (A) | 0 10000011 11111100000000000000000 | (B) | 0 10000111 11111100000000000000000 |
|  | (C) | 0 10000110 11111100000000000000000 | (D) | 0 10000010 11111100000000000000000 |

〈試題作答結束〉